## Slide 1: Prediction of Generalized Chiller Efficiency by using Machine Learning Method
Andrew Copsey*, Kailei Liu**,Hongbo Qiao*.
* Department of Materials Science and Engineering ** Department of Chemical Engineering
Introduction
Results
Data Cleaning and ML Model
Centrifugal chillers are large, centralized refrigeration machines often used to generate cooling for large HVAC systems. Chillers are generally custom-built based on customer requirements with a variety of bundle sizes and motor sizes, which makes a general prediction of chiller electrical efficiency difficult.
Current Issue:
Existing Model cannot accurately predict different chiller efficiency based on the existing dataset.
Goals:
Build a model to predict a new chiller efficiency based on the exist chiller performance and design specifications.
Data cleaning
Machine Learning Models
Create a wrap function
Data Cleaning & Model Selection
Auditable Equation
Raw Data
Time Series Data
Non-numeric Features
50+ features/chiller
Date Screening
Feature Elimination
Data Numeralization
Model Comparison
Piecewise & Polynomial Fit
Polynomial Fit
By fitting the data with different methods, we find that the polynomial regression have a better and more reasonable result among the 5 methods mentioned above.
By fitting with 24 unique chillers (58 in total) datasets we have , the polynomial function fitted the data very well.
*
As a result, we have a polynomial function fitted the data very well with good performances and excellent statistic data.
But due to the limited chiller design specification data and the unknown environment factors, the model isn’t perfect and still need to be further investigate.
Linear Fit
 | Neural | Linear
RMSE | 0.4 - 1000 | 0.7 - 1000
R^2 | 0.1 – 0.97 | 0.3 - 0.9
Linear
Or
Polynomial
Neural Network
Piecewise
Or
Non-Piecewise
 | RMSE | R^2
Polynomial** | 0.023944 | 0.92
Linear | 0.2 - 0.7 | 0.88**
* An Example of Equation
** Specific Data to one chiller
Notes: MSE